## Slide 1: Lecture 3 - BCH Codes (a class of codes for multi-errors correction)
In this lecture we will
go through an example, BCH(10,6) code for double error correcting
explain next assessed programming task
– implementing BCH(10,6)
Note that, all calculations here use “mod 11”

## Slide 2: BCH codes
First discovered by Hocquenghem in 1959 and independently by Bose and Ray-Chaudhuri in 1960. Name BCH is from the first letter of three inventors.
BCH codes form a large class of multiple random error correcting codes
Widely used. e.g. CD player, Voyager 2 spacecraft , …

## Slide 3: Vandermonde Matrix
A matrix has the form shown on the right is called Vandermonde matrix where a1a2,…an are distinct non-zero element of a field.
(we will explain the word field in the next tutorial)

## Slide 4: A Vandermonde Matrix using the field {1,2,3,….10} (i.e. mod 11)
1 1 1 1 1 1 1 1 1 1
1 2 3 4 5 6 7 8 9 10

## Slide 5: BCH codes use Vandermonde Matrix for parity checking matrix
For example, BCH(10,6) is a code over GF(11)
It can correct double error and detect triple error
Its parity check matrix is on the left
The first 2 rows are same as H in the single error correcting code given last week.

## Slide 6: Generator Matrix and Encoding
G is derived from H (we skip this tedious process )
G generates parity bits so that all check-sum results are 0.
Encode 6 digits x by G
encode(x) = x*G (mod 11)
d7 = (4d1+10d2+9d3+2d4+d5+7d6) mod 11
d8= (7d1+8d2+7d3+d4+9d5+6d6) mod 11
d9 = (9d1+d2+7d3+8d4+7d5+7d6) mod 11
d10 = (d1+2d2+9d3+10d4+4d5+d6) mod 11

## Slide 7: Generator Matrix and Encoding An example
Let Input x = 888888  8888880747
d7 = (4*8+10*8+9*8+2*8+8+7*8) mod 11 = 264 mod 11 = 0
d8 = (7*8+8*8+7*8+8+9*8+6*8) mod 11 = 304 mod 11 = 7
d9 = (9*8+8+7*8+8*8+7*8+7*8) mod 11 = 312 mod 11 = 4
d10 = (8+2*8+9*8+10*8+4*8+8) mod 11 = 216 mod 11 = 7
Check if every parity row is 0 under mod 11 (ref. H in slide 5)
  row 1: 8*6+7+4+7 = 66 = 0 mod 11
  row 2: 8*(1+2+3+4+5+6)+8*7+9*4+10*7=330 = 0 mod 11
  row 3: 8*(1+4+9+5+3+3)+9*7+4*4+7 = 286 = 0 mod 11
  row 4: 8*(1+8+5+9+4+7)+6*7+3*4+10*7 = 396 = 0 mod 11

## Slide 8: Encoding by Generator Matrix (another example shown by matrix multiplication)
y1 = x1, y2 = x2, y3 = x3, y4 = x4, y5 = x5, y6 = x6
y7 = (4+10+9+2+1+7) mod 11 = 33 mod 11 = 0
y8 = (7+8+7+8+9+6) mod 11 = 38 mod 11 = 5
y9 = (9+1+7+8+7+7) mod 11 = 39 mod 11 = 6
y10 = (1+2+9+10+4+1) mod 11 = 27 mod 11 = 5
1 0 0 0 0 0 4 7 9 1
0 1 0 0 0 0 10 8 1 2
0 0 1 0 0 0 9 7 7 9
0 0 0 1 0 0 2 1 8 10
0 0 0 0 1 0 1 9 7 4
0 0 0 0 0 1 7 6 7 1
x = 111111
y is encoded x
y = ( 1 1 1 1 1 1 ) *
= ( 1 1 1 1 1 1 0 5 6 5 )

## Slide 9: An issue with “mod 11”
The four checking digits, d7-d10, can be ‘10’, which needs two digits to represent.
Solution in ISBN – using ‘X’
Another solution – simply abundant the number which produce ‘10’s. (current solution)
An example: input = 000009
  d7 = (4d1+10d2+9d3+2d4+d5+7d6) mod 11 = 7*9 mod 11 = 8
  d8= (7d1+8d2+7d3+d4+9d5+6d6) mod 11 = 6*6 mod 11 = 10 
  d9 = (9d1+d2+7d3+8d4+7d5+7d6) mod 11 = 7*9 mod 11 = 8
  d10 = (d1+2d2+9d3+10d4+4d5+d6) mod 11 = 9
Output would be 00000981089
Can we use mod 10 instead?

## Slide 10: Decoding Steps (error correction)
From 10 digit, d1, d2, …d10
generate 4 digit syndromes (s1, s2 , s3 , s4)
Use syndromes to identify if there are errors:
if (s1, s2 , s3 , s4)==(0,0,0,0), no error
else work out single/double errors and correct them

## Slide 11: How to work out 4 digit syndromes (s1,s2,s3,s4) – using the parity checking matrix given in slide 5
s1= (d1+d2+d3+d4+d5+d6+d7+d8+d9+d10) mod 11
s2= (d1+2*d2+3*d3+4*d4+5*d5+6*d6+7*d7+8*d8+9*d9
+10*d10) mod 11
s3= (d1+22*d2+32*d3+42*d4+52*d5+62*d6+72*d7+82*d8
+92*d9+102*d10) mod 11
= (d1+4*d2+9*d3+5*d4+3*d5+3*d6+5*d7+9*d8
+4*d9+d10) mod 11
s4= (d1+23*d2+33*d3+43*d4+53*d5+63*d6+73*d7+83*d8
+93*d9+103*d10) mod 11
= (d1+8*d2+5*d3+9*d4+4*d5+7*d6+2*d7+6*d8
+3*d9+10*d10) mod 11

## Slide 12: Decoding – after worked out syndromes
S1 S2
S3 S4
We are interested in working out:
P = S22 - S1 S3
Q = S1 S4 - S2 S3
R = S32 - S2 S4
because when all P,Q, and R are zeros, we know that there is a single error.

## Slide 13: Decoding – More Details
Let’s assume that there is a single error of magnitude a in position i, (i=5 for example)
s1 = (d1+d2+d3+d4+d5+a+d6+d7+d8+d9+d10) mod 11
s2= (d1+2*d2+3*d3+4*d4+5*d5 +5*a+6*d6+7*d7+8*d8+9*d9
+10*d10) mod 11
as (d1+d2+d3+d4+d5+d6+d7+d8+d9+d10) mod 11 = 0
we get error magnitude a = s1
similarly, error position i = s2/a = s2/s1
(ref last week’s lecture for single error correction)

## Slide 14: Decoding – More Details
When there are two errors, we need to work out 4 information:
two positions (i, j) and
two error magnitudes (a, b).
i = (- Q + √(Q2-4*P*R)) / 2*P
j = (- Q - √(Q2-4*P*R)) / 2*P
b = (i*s1- s2) / (i - j)
a = s1 – b

## Slide 15: Decode from 4 digit syndromes (s1,s2,s3,s4) - proof
For i=1,2,…10
s1=Σ di = d1+d2+…….+d10
s2=Σ i*xi
s3=Σ i2xi
s4=Σ i3xi
If (s1,s2,s3,s4) =(0,0,0,0),
 no errors
What if there two errors?
Need 4 information:
two positions (i,j) and
two magnitudes (a,b).
Suppose two errors of and j respectively. Then
a + b = s1 (1)
i*a + j*b = s2 (2)
i2*a + j2*b = s3 (3)
i3*a + j3*b = s4 (4)
Thus, to find a,b,i, and j is to solve these 4 equations. Note that they are non-linear equations.

## Slide 16: Decode from 4-digit syndromes (s1,s2,s3,s4) - proof cont.
To solve
a + b = s1 (1)
i*a + j*b = s2 (2)
i2*a + j2*b = s3 (3)
i3*a + j3*b = s4 (4)
First we try to eliminate a,b,j:
i x (1) – (2) gives
b(i-j)=is1-s2 (5)
i x (2) – (3) gives
bj(i-j)=is2-s3 (6)
i x (3) – (4) gives
bj2(i-j)=is3-s4 (7)
Computing (6)2
b2j2(i-j)2=(is2-s3 )2
Computing (5)x(7)
b2j2(i-j)2=(is1-s2)x(is3-s4)
Therefore, we get
(is2-s3 )2=(is1-s2)x(is3-s4)
So,
(is2-s3 )2 - (is1-s2)x(is3-s4) = 0
Expand the left side, we get
(s22 - s1s3)i2 +
(s1s4 - s2s3)i +
(s32-s2s4 ) = 0

## Slide 17: Decode from 4-digit syndromes (s1,s2,s3,s4) - proof cont.
Now, we need to solve this quadratic equation:
(s22 - s1s3)i2 +
(s1s4 - s2s3)i +
(s32 - s2s4 ) = 0
Let
P = (s22 - s1s3)
Q = (s1s4 - s2s3)
R = (s32-s2s4 )
The equation is
Pi2+Qi+R = 0 (8)
Let’s start from a case: only ONE error, i.e. b = 0. In this case, 4 equations (1) to (4) are simplified to:
a = s1 ,, i*a = s2 ,
i2*a = s3 , i3*a = s4
Substitute the above to P,Q, and R, we get P=Q=R=0.
Therefore, when P,Q,R are all zeros, we know there is only a single error.

## Slide 18: Decode from 4-digit syndromes (s1,s2,s3,s4)
When P=Q=R=0,
we assume that a single
error of magnitude s1 in
position s2/s1
This is because
a = s1 ,and i*a = s2 ,
So i = s2/s1
When P,Q,R, are not all 0,
Two roots for
Pi2+Qi+R = 0 (8)
will be i and j:
i,j = (- Q ± √(Q2-4PR)) / 2P (9)
from (5) we get
b = (i*s1- s2) / (i - j) (10)
from (10), we get
a = s1 – b (11)
end of proof

## Slide 19: Summary on BCH(10,6)
Encoding – for every 6 digits input, use the following formulas to generate 4 parity checking digits. Need to check no 10 in d7 d8 d9 d10
d7 = (4d1+10d2+9d3+2d4+d5+7d6) mod 11
d8= (7d1+8d2+7d3+d4+9d5+6d6) mod 11
d9 = (9d1+d2+7d3+8d4+7d5+7d6) mod 11
d10 = (d1+2d2+9d3+10d4+4d5+d6) mod 11
Decoding – for every 10 digits input, use the following formulas to generate 4 syndromes, s1s2s3s4
s1= (d1+d2+d3+d4+d5+d6+d7+d8+d9+d10) mod 11
s2= (d1+2*d2+3*d3+4*d4+5*d5+6*d6+7*d7+8*d8+9*d9 +10*d10) mod 11
s3= (d1+4*d2+9*d3+5*d4+3*d5+3*d6+5*d7+9*d8+4*d9+d10) mod 11
s4= (d1+8*d2+5*d3+9*d4+4*d5+7*d6+2*d7+6*d8+3*d9+10*d10) mod 11

## Slide 20: Cont. Summary on BCH(10,6)
There are FOUR cases need to handle after calculating syndromes:
no error: s1s2s3s4 = 0000
2. Calculate, P,Q,R (using formulas in slide 12)
if P=Q=R=0, there is a single error at position s2/s1, and the magnitude is s1.
3. When P,Q,R are not all zeros, it is double error case.
Solve i,j = (- Q ± √(Q2-4*P*R)) / 2*P
to work out error positions i, j, then work out a, and b:
b = (i*s1- s2) / (i - j)
a = s1 – b
4. If (Q2-4*P*R) doesn’t have a square root (under mod 11) , or
if position value i or j is zero, or one of d1-d10 is corrected into 10
there are at least three errors have occurred.

## Slide 21: Go through a decode example by hand
A 10-digit 8888880747 transmitted to 8899880747 (2 errors)
s1 = 8+8+9+9+8+8+0+7+4+7 mod 11 = 2
s2 = 8+2*8+3*9+4*9+5*8+6*8+8*7+9*4+10*7 mod 11 = 7
s3 = 8+4*8+9*9+5*9+3*8+3*8+9*7+4*4+1*7 mod 11 = 3
s4 = 8+8*8+5*9+9*9+4*8+7*8+6*7+3*4+10*7 mod 11 = 3
P = (7*7-2*3) mod 11 = 43 mod 11 = 10
Q = (2*3-7*3) mod 11 = -15 mod 11 = -4 mod 11 = 7
R = (3*3-7*3) mod 11 = - 12 mod 11 = -1 mod 11 = 10
Q*Q – 4PR = -351 mod 11 = -10 mod 11 = 1, √1 = 1
i = ((-7+1)/20) mod 11 = -6/9 mod 11 = 5*5 mod 11 = 3
j = ((-7-1)/20) mod 11= -8*5 mod 11 = 3*5 mod 11 = 4
b = (3*2-7)/(3-4) mod 11 = -1/-1 mod 11 = 10*10 mod 11=1,
a = 2-1 = 1 done!

## Slide 22: Other Error Correction Codes close toThe Shannon Limit
Turbo Codes - high-performance error correction codes (1993), no Cliff effect. Has a wider range of applications, mainly in wireless communication, ranging from the 3G, 4G mobile systems to deep-space and satellite communications.
Low Density Parity Checking Code (LDPC)

## Slide 23: Appendix – a filed Zn Zn = {0,1,2,…,n-1} where n is prime
E.g. GF(11), n=11, Z11 = {0,1,2,3,4,5,6,7,8,9,10}
x | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
-x | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
x2 | 1 | 4 | 9 | 5 | 3 | 3 | 5 | 9 | 4 | 1
√x | 1 |  | 5 | 2 | 4 |  |  |  | 3 | 
x-1 | 1 | 6 | 4 | 3 | 9 | 2 | 8 | 7 | 5 | 10

## Slide 24: This week’s practical
Implement BCH(10,4) code, both encoding and decoding:
Read 6 digits, generate its 10 digits BCH code. Need to recognise unusable code (last week’s task)
Read 10 digits BCH code, then correct errors if any. In case of more than 2 errors it should detect it
GUI is not required, but strongly recommend